## Slide 1: HARDWARE IMPLEMENTATION OF HOPFIELD NEURAL NETWORK

## Slide 2: Points in favor of hardware implementation
Inherent parallelism and connectionist model of ANN’s which find a natural application through hardware. General purpose processors operate sequentially.
Simple ANN models require simple, low precision computations which can be performed faster on cheap and low precision hardware.
Also since hardware is getting cheaper by the day, custom hardware can be built to perform complex computations.

## Slide 3: Why FPGA?
FPGAs are a form of programmable logic, which offer flexibility in design like software, but with performance speeds closer to Application Specific Integrated Circuits (ASICs).
With the ability to be reconfigured an endless amount of times after it has already been manufactured

## Slide 4: XILINX FPGA
Xilinx has traditionally manufactured SRAM-based FPGAs; so- called because the programmable resources3 for this type of FPGA are controlled by static RAM cells.
It consists of Configurable Logic Blocks (CLBs)
General Architecture of Xilinx FPGAs.

## Slide 5: A SURVEY OF HARDWARE IMPLEMENTATIONS OF ARTIFICIAL NEURAL NETWORKS

## Slide 6: Comparison between analog and digital implementations of ANNs
People are more familiar with digital design now i.e. analog design is an uncommon capability.
Most applications comprise of digital systems and a digital neural network will provide ease in integration with these systems.
Signal interconnection is also a problem.
The solution has to be multiplexing of connections i.e. multiple synaptic connections share the same wire.
Analog designs are hard to multiplex.

## Slide 7: Amadahl’s law

## Slide 8: Hardware implementations using FPGAs
Why Reconfiguration?
- To exploit concurrency and rapidly reconfigure for weight and topology adaptation.

## Slide 9: Different implementation approaches possible due to Reconfiguration
Prototyping and simulation
  to test various ANN implementations and learning algorithms.
Density enhancement
  increase in the functional capacity per unit area of the chip
  -Time multiplex an FPGA chip
  -Dynamic constant folding
Topology adaptation

## Slide 10: FPGA IMPLEMENTATION ISSUES

## Slide 11: FPGA implementations of neural networks can be classified on the basis of:
1. Learning Algorithm
2. Signal representation
3. Multiplier reduction schemes

## Slide 12: Learning algorithm
The type of neural network used in FPGA-based implementations is an important feature used in classifying such architectures. The type of neural network applied depends on the intended application used to solve the problem at hand.
Various types of Neural Networks
Back propagation Algorithm
Ontogenic Neural Networks
Cellular Automata based neural networks
Modular Neural Networks

## Slide 13: Signal Representation
Frequency-based
Spike Train
Floating-point
Fixed-point

## Slide 14
Fixed Point is most popular signal representation used among all the surveyed FPGA-based (i.e. digital) ANN architectures.
Merits:
-more area efficient than floating-point
-is not as severely limited in range-precision as both, frequency and spike-train signal representations
Issues:
-Overflow and underflow -Convergence rates -Quality of generalization
Solution:
-Determining the minimum allowable precision and minimum allowable range
-Holt and Baker showed that 16-bit fixed- point was the minimum allowable range-precision for the back propagation algorithm

## Slide 15: Multiplier Reduction Schemes
Use of bit-serial multipliers
  bit-serial can scale up to a signal representation of any range-precision
Reduce range-precision of multiplier
  this is not a feasible approach as it has a negative effect on convergence rates
Signal representations that eliminate the need for multipliers
  using a stochastic-based spike train signal
  Implementation of variant of REMAP for use with Sparse Distributed Memory (SDM) ANN types

## Slide 16: IMPLEMENTATION APPROACHES

## Slide 17
Iteration
Reiterate the Forward and Backward Computations for each training example in the epoch. The trainer can continue to train the ANN using one or more epoch until some stopping criteria (eg. low error) is met.
Once training is complete, the ANN only needs to carry out the Forward Computation when used in application.

## Slide 18: Implemenation approaches
Basically when implementing the back propagation algorithms on FPGAs there are two approaches
Non-RTR Approach
RTR (Run-Time-Reconfiguration) Approach